## Slide 1
InternalCharger: Firmware Features
Will NOT begin until the user has made a non-negligible duration of
consistent contact with the terminals that power it
Prevents more than 3A from going to an individual cell
Can communicate its status to the powerboard as a slave
Will NOT charge a battery that has discharged dangerously low (less than 2.5V/cell * 4cells => 6V).
Notes: Requirements
Special Cases:
- what if one cell gets more than it’s maximum share (3A)?
- is the other battery charging it too much?
- is it too discharged?
Charging IC:
- the charging IC needs to be refreshed with the charging configuration
(charging voltage, max charging current, etc) every 170s or less or
else it will time out
SBS-Compliant Batteries:
- the smart battery needs to be polled every 10 seconds (and not faster) to
avoid missing critical broadcasts (such as AlarmWarning) and not consume
too much bandwidth
- perform an update within 5s of when a monitored parameter changes?
- if a Li-ion battery is stored in a discharged condition The boost feature applies a small charge current to activate the protection circuit to 2.20–2.90V/ cell, at which point a normal charge commences.
Caution should be applied not to boost lithium-based batteries back to life that have dwelled below 1.5V/cell for a week or longer
http://en.wikipedia.org/wiki/Lithium-ion_battery#Battery_charging_procedure

## Slide 2
one side just wants too much,
so limit the overall current to the
Individual limit
InternalCharger: State Diagram
Sleeping
Charging
start
(VCELLA < 16V OR VCELLB < 16V) AND
(6V < VCELLA AND 6V < VCELLB)
- update our status variable to
‘alive and on dock’ (for Tx
to powerboard)
- turn on the charging IC
- connect cell A
- connect cell B
- configure charger to Vcharge,max = 16.5V, Icharge,max = 6A
Charger refresh timer expired
- start the charger refresh timer
- configure the charger
IcellA < 100mA
- disconnect cell A
IcellB < 100mA
- disconnect cell B
ICELLA < 100mA AND_ICELLB < 100mA
- turn off the charging IC
- re-connect each cell to monitor the
SOC via their voltages
3A < IcellA OR 3A < IcellB
- disconnect any cell that is
accepting too much current
- turn off the charging IC
- start cooldown timer
Investigating
Overcurrent
cooldown timer expired AND
(250mA < IcellA OR 250mA < IcellB)
- turn on RED LED to indicate an error
- turn off everything
cooldown timer expired AND
(IcellA < 250mA AND IcellB < 250mA)
- turn on charging IC
- Icharge,max = 3A
Awakening
- start awakening timer
awakening timer expired
disconnect a cell if it
begins charging the other
Hanging
6V < VCELLA OR 6V < VCELLB
- turn off everything
- turn on RED LED to indicate an error
Notes: Requirements
Special Cases:
- what if one cell gets more than it’s maximum share (3A)?
- is the other battery charging it too much?
- is it too discharged?
Charging IC:
- the charging IC needs to be refreshed with the charging configuration
(charging voltage, max charging current, etc) every 170s or less or
else it will time out
SBS-Compliant Batteries:
- the smart battery needs to be polled every 10 seconds (and not faster) to
avoid missing critical broadcasts (such as AlarmWarning) and not consume
too much bandwidth
- perform an update within 5s of when a monitored parameter changes?
- if a Li-ion battery is stored in a discharged condition The boost feature applies a small charge current to activate the protection circuit to 2.20–2.90V/ cell, at which point a normal charge commences.
Caution should be applied not to boost lithium-based batteries back to life that have dwelled below 1.5V/cell for a week or longer
http://en.wikipedia.org/wiki/Lithium-ion_battery#Battery_charging_procedure

## Slide 3
State Diagram Legend
My state 2
start
My state 1
(gerund, ‘ing-suffix’)
My event
- my service 1
- my service 2
…
- my service n
Notes:
- use a two-space hanging indent
to list services
- underline the event
- use a gerund in the state description
short clarifying comment
Notes: Requirements
Special Cases:
- what if one cell gets more than it’s maximum share (3A)?
- is the other battery charging it too much?
- is it too discharged?
Charging IC:
- the charging IC needs to be refreshed with the charging configuration
(charging voltage, max charging current, etc) every 170s or less or
else it will time out
SBS-Compliant Batteries:
- the smart battery needs to be polled every 10 seconds (and not faster) to
avoid missing critical broadcasts (such as AlarmWarning) and not consume
too much bandwidth
- perform an update within 5s of when a monitored parameter changes?
- if a Li-ion battery is stored in a discharged condition The boost feature applies a small charge current to activate the protection circuit to 2.20–2.90V/ cell, at which point a normal charge commences.
Caution should be applied not to boost lithium-based batteries back to life that have dwelled below 1.5V/cell for a week or longer
http://en.wikipedia.org/wiki/Lithium-ion_battery#Battery_charging_procedure