## Slide 1
InternalCharger: Firmware Features
Will NOT begin until the user has made stable contact with the terminals that power it
Safeguards against an internal short (seen as voltage never rising)
Safeguards against a deeply-discharged side (initially charges at lower current)
At each state, safeguards against short?
Prevents more than 3A from going to an individual cell at all times
Can communicate its status to the powerboard as a slave
Notes: Requirements
Special Cases:
- what if one cell gets more than it’s maximum share (3A)?
- is the other battery charging it too much?
- is it too discharged?
Charging IC:
- the charging IC needs to be refreshed with the charging configuration
(charging voltage, max charging current, etc) every 170s or less or
else it will time out
SBS-Compliant Batteries:
- the smart battery needs to be polled every 10 seconds (and not faster) to
avoid missing critical broadcasts (such as AlarmWarning) and not consume
too much bandwidth
- perform an update within 5s of when a monitored parameter changes?
- if a Li-ion battery is stored in a discharged condition The boost feature applies a small charge current to activate the protection circuit to 2.20–2.90V/ cell, at which point a normal charge commences.
Caution should be applied not to boost lithium-based batteries back to life that have dwelled below 1.5V/cell for a week or longer
http://en.wikipedia.org/wiki/Lithium-ion_battery#Battery_charging_procedure

## Slide 2
State Diagram Legend
My state 2
start
My state 1
(gerund, ‘ing-suffix’)
My event
- my service 1
- my service 2
…
- my service n
Notes:
- use a two-space hanging indent
to list services
- underline the event
- use a gerund in the state description
short clarifying comment
Notes: Requirements
Special Cases:
- what if one cell gets more than it’s maximum share (3A)?
- is the other battery charging it too much?
- is it too discharged?
Charging IC:
- the charging IC needs to be refreshed with the charging configuration
(charging voltage, max charging current, etc) every 170s or less or
else it will time out
SBS-Compliant Batteries:
- the smart battery needs to be polled every 10 seconds (and not faster) to
avoid missing critical broadcasts (such as AlarmWarning) and not consume
too much bandwidth
- perform an update within 5s of when a monitored parameter changes?
- if a Li-ion battery is stored in a discharged condition The boost feature applies a small charge current to activate the protection circuit to 2.20–2.90V/ cell, at which point a normal charge commences.
Caution should be applied not to boost lithium-based batteries back to life that have dwelled below 1.5V/cell for a week or longer
http://en.wikipedia.org/wiki/Lithium-ion_battery#Battery_charging_procedure

## Slide 3
InternalCharger: State Diagram
Charging
start
3A < IsideA OR 3A < IsideB
- disconnect both sides
- start cooldown timer (~100ms)
Investigating Overcurrent
cooldown timer expired AND
(0 < IsideA OR 0 < IsideB)
- turn off everything
- start awakening timer (~1m)
cooldown timer expired AND
(IsideA ~= 0A AND IsideB ~= 0A)
- decrement Icharge,max, to a limit
- configure charger
- reconnect both sides
- delay long enough to get a new A/D reading
Awakening
- start awakening timer
awakening timer expired
- status = ‘alive and on dock’
- turn on the charging IC
- Icharge,max = min(0.1/h*C, 3A/side)
- configure charger
- delay to ensure charger is ready
- connect sideA and sideB
- delay to ensure valid current readings
- start charger refresh timer (0s)
- start revive safety timer (~10s)
Notes:
- the current sensor produces 0V if
current flows in the reverse direction
- the maximum current the smart
battery can accept is 3A on each side
- there are four (4) cells per side
- consider the duty cycle of a bad
situation
- the limit to power the robot is ~1.5A
Reviving
3V/cell < VsideA AND 3V/cell < VsideB
- Icharge,max = min(0.7/h*C, 3A/side)
revive-safety timer expired AND
(VsideA == 0 OR VsideB == 0V)
- disconnect sideA and sideB
- start awakening timer (~1m)
IsideB ~= 0
- disconnect sideB
- connect sideA
- start balance timer (~10s)
IsideA ~= 0
- disconnect sideA
- connect sideB
- start balance timer (~10s)
balance timer expired
- start balance-check timer (~100ms)
- connect sideA and sideB
charger-refresh timer expired
- start the charger refresh timer (~10s)
- increment the overall current (Icharge,max) to slowly float
up to the maximum in case it was ever decremented
- configure charger with potentially updated Icharge,max
Balancing
3A < IsideA OR 3A < IsideB
- disconnect both sides
- start cooldown timer (~100ms)
balance-check timer expired AND
(0 < IsideA AND 0 < IsideB)
balance-check timer expired AND
(IsideA < 0 OR IsideB < 0)
- disconnect the side that is drawing no current
- start balance timer (~10s)
Checking Balance
Won’t catch overcurrent here, but short enough to be OK