## Slide 1
Powerboard: Firmware Features
Controls the left drive motor, right drive motor and flipper motor
Recovers after an accidental overcurrenting of the batteries
Prevents a current spike by tapering sharp motor speed transitions
Wraps the drive motors in independent control loops
Monitors the battery condition, including state-of-charge and alarm warnings
Communicates state-of-charge of both sides to software through designated USB registers
Notes: Requirements
Special Cases:
- what if one cell gets more than it’s maximum share (3A)?
- is the other battery charging it too much?
- is it too discharged?
Charging IC:
- the charging IC needs to be refreshed with the charging configuration
(charging voltage, max charging current, etc) every 170s or less or
else it will time out
SBS-Compliant Batteries:
- the smart battery needs to be polled every 10 seconds (and not faster) to
avoid missing critical broadcasts (such as AlarmWarning) and not consume
too much bandwidth
- perform an update within 5s of when a monitored parameter changes?
- if a Li-ion battery is stored in a discharged condition The boost feature applies a small charge current to activate the protection circuit to 2.20–2.90V/ cell, at which point a normal charge commences.
Caution should be applied not to boost lithium-based batteries back to life that have dwelled below 1.5V/cell for a week or longer
http://en.wikipedia.org/wiki/Lithium-ion_battery#Battery_charging_procedure

## Slide 2
State Diagram Legend
My state 2
start
My state 1
(gerund, ‘ing-suffix’)
My event
- my service 1
- my service 2
…
- my service n
Notes:
- use a two-space hanging indent
to list services
- underline the event
- use a gerund in the state description
short clarifying comment if needed
Notes: Requirements
Special Cases:
- what if one cell gets more than it’s maximum share (3A)?
- is the other battery charging it too much?
- is it too discharged?
Charging IC:
- the charging IC needs to be refreshed with the charging configuration
(charging voltage, max charging current, etc) every 170s or less or
else it will time out
SBS-Compliant Batteries:
- the smart battery needs to be polled every 10 seconds (and not faster) to
avoid missing critical broadcasts (such as AlarmWarning) and not consume
too much bandwidth
- perform an update within 5s of when a monitored parameter changes?
- if a Li-ion battery is stored in a discharged condition The boost feature applies a small charge current to activate the protection circuit to 2.20–2.90V/ cell, at which point a normal charge commences.
Caution should be applied not to boost lithium-based batteries back to life that have dwelled below 1.5V/cell for a week or longer
http://en.wikipedia.org/wiki/Lithium-ion_battery#Battery_charging_procedure

## Slide 3
Powerboard: State Diagram
Charging
start
3A < IsideA OR 3A < IsideB
- disconnect both sides
- start cooldown timer (~100ms)
Investigating Overcurrent
cooldown timer expired AND
(0 < IsideA OR 0 < IsideB)
- turn off everything
- start awakening timer (~1m)
cooldown timer expired AND
(IsideA ~= 0A AND IsideB ~= 0A)
- decrement Icharge,max, to a limit
- configure charger
- reconnect both sides
- delay long enough to get a new A/D reading
Initializing
- bring up battery slowly (blocking)
- turn on power bus
Notes:
- the current sensor produces 0V if
current flows in the reverse direction
- the maximum current the smart
battery can accept is 3A on each side
- there are four (4) cells per side
- consider the duty cycle of a bad
situation
- the limit to power the robot is ~1.5A
Reviving
3V/cell < VsideA AND 3V/cell < VsideB
- Icharge,max = min(0.7/h*C, 3A/side)
revive-safety timer expired AND
(VsideA == 0 OR VsideB == 0V)
- disconnect sideA and sideB
- start awakening timer (~1m)
IsideB ~= 0
- disconnect sideB
- connect sideA
- start balance timer (~10s)
IsideA ~= 0
- disconnect sideA
- connect sideB
- start balance timer (~10s)
balance timer expired
- start balance-check timer (~100ms)
- connect sideA and sideB
SoC-check timer expired
- start the SoC-check timer (~10s)
Balancing
3A < IsideA OR 3A < IsideB
- disconnect both sides
- start cooldown timer (~100ms)
balance-check timer expired AND
(0 < IsideA AND 0 < IsideB)
balance-check timer expired AND
(IsideA < 0 OR IsideB < 0)
- disconnect the side that is drawing no current
- start balance timer (~10s)
Checking Balance
Won’t catch overcurrent here, but short enough to be OK
Battery up AND software up
- connect motors