## Slide 1
Sleeping
Charging
start
InternalCharger State Diagram
VCELLA < 16V OR VCELLB < 16V AND
(TcellA < HOT AND TcellA < HOT)
- turn on the charging IC
- connect cell A
- connect cell B
Charger refresh timer expired
- start the charger refresh timer
- configure the charge limits
IcellA < 100mA
- disconnect cell A
IcellB < 100mA
- disconnect cell B
ICELLA < 100mA AND_ICELLB < 100mA
- turn off the charging IC
- re-connect each cell to monitor the
SOC via their voltages
HOT < TcellA OR_HOT < TcellA
- turn off the charging IC
- disconnect both cells
Notes: Requirements
Charging IC:
- the charging IC needs to be refreshed with the charging configuration
(charging voltage, max charging current, etc) every 170s or less or
else it will time out
SBS-Compliant Batteries:
- the smart battery needs to be polled every 10 seconds (and not faster) to
avoid missing critical broadcasts (such as AlarmWarning) and not consume
too much bandwidth
- perform an update within 5s of when a monitored parameter changes?
Current(), AverageCurrent(), Voltage(), and Temperature()